Description of specifications:

- PONZI ASD 1 -

AUTOMATIC SLIDING DOOR WITH A SINGLE WING PROFILES PONZI SERIES THERMAL CUT

AUTOMATIC SLIDING DOOR PONZI ASD 1

PROFILES PONZI SERIES THERMAL CUT

Made in a single mirror that opens automatically.

The door is made of extruded aluminium alloy profiles with thermal break - rounded Ponzi accident-prevention series - surface finish made with an oven-painted or anodic electrolytic treatment (colour to choose from our sample book), laminated accident-proof glass 44 mm thick 8/9 composed of two 4 mm clear transparent float plates with interposed pvb film from 0.76 mm. (Also available with insulating double glazing up to a maximum thickness of 45 mm). Special gaskets with relative counter-profiles for thermo-acoustic sealing.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 Stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys for door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable box in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS).

• N. 2 combined radar (motion and presence sensor).

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it