Tender Descriptive:

- PONZI      TOS 1 -

PROFILES PONZI SERIES 50 mm STORED ACCIDENT PREVENTION

AUTOMATIC         SLIDING       DOOR          FOR        ESCAPE     ROUTES         WITH  A  SLIDING            WINGS PROFILES PONZI        SERIES      50  mm  STORED  ACCIDENT       PREVENTION

Made in a single mirror that opens automatically.

The door is made of extruded aluminum alloy sections of 50 mm - rounded Ponzi accident-prevention series - surface finish made with an oven-painted or anodic electro-coloring treatment (color to choose from our sample book), laminated accident-proof glass 44 mm thick 8/9 composed of two 4 mm clear transparent float plates with interposed pvb film from 0.76 mm. (Also available with insulating double glazing up to a maximum thickness of 36 mm). Special gaskets with the relative counter-profiles for the thermo-acoustic seal.

The automatism consists of:

	N. 1 Low voltage gear motor.

	N. 1 stabilized power supply.

	N. 1 Microprocessor control board.

	N. 1 extruded aluminum track.

	N. 2 carrier trolleys per door.

	N. 1 adapter profile for suspension leaf.

	N. 1 Multi-function battery pack

	N. 1 bistable electric lock.

	Inspectable casing in extruded aluminum (H = 155 mm).

	N. 1 Function selector with 5 positions (KS).

	N. 2 combined radar (motion and presence sensor).

TOS BREACHING ANTI-PANIC DEVICE

In the event of an emergency, the sliding leaf- in normal operation - can be tilted to the outside in any position it is, with a simple pressure at any point of the same, even when in motion.

The system, by means of guides fixed to the floor, allows the leaf to swing open, disabling the automatic function until the function is restored. This opening system therefore assumes the function of an anti-panic device and a safety exit and complies with the most recent regulations on pedestrian automatic closures installed on escape routes (EN 16005; DM 10 March 1998 - annex III; Legislative Decree 81/2008).

NB: To carry out the breakout function for the escape route even with the door moving, it is essential that the mechanism is positioned outside the compartment.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25 Tel. +39 02 8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it	info@ponzi-in.it